## Slide 1
Planning for Future Water and Smart Water Management in Taiwan
Dr. Chien-Hsin Lai, Director-General Water Resources Agency (WRA),
Ministry of Economic Affairs (MOEA)
  Global Water Summit

## Slide 2: Outline
I、 Challenges
II、Water Problems in Taiwan
III、Effective Management

## Slide 3
Global Urban Population Growth(1950 ~ 2050)
I、Challenges
Urban population growth is a global trend
Source: World Economic Forum calculation based on World Urbanization Prospects(2014 revision)data.
Chart: billions
| 1950 | 2000 | 2050
Urban population(left scale) | 1.3 | 2.7 | 6.3
Share of urban population in total population(right scale) | 29 | 45 | 67

## Slide 4
Taiwan has the same trend….
Taiwan population space change
The population is gradually concentrated in north, central and south metropolitan areas
1970
1990
2010
Taipei City
Increase on water demand and discharge could exceed urban capacity
20 million
23million
15 million

## Slide 5
Due to natural environment and artificial interference,
Source：ETtoday、Liberty times、United Daily News、EPA
Flood
Drought
Poor quality
The rainfall in typhoon Morakot reached 2327mm in two days (Alishan station)
Zengwen reservoir had no rainfall for more than 250 days
Heavy pollution in rivers 633.4KM(21.6%)
Water problems in Taiwan…
II、Water Problems in Taiwan

## Slide 6
III、Effective Management
Municipal
Agriculture
Industry
Catchment Conservation
Water Source Protection
Reservoir Management
water source management
water supply management
Client management
Water purification
Water supply system
Rain water recycling
Seawater desalination
Reclaimed water
Diversified water sources
Cross-regional deployment
Reserve water supply
Dispatching backup

## Slide 7
1. Land use control in the reservoir catchment
Taiwan has set up 114 water quality and quantity conservation areas.
Strictly control land use and development.
Compensation mechanism for restricted areas.
Protection zone of water quality and quantity of tap water
Conservation areas

## Slide 8
Strengthening dredging and sediment-sluicing facilities in 13 major reservoirs
2. Maintain reservoir capacity
Hydrosuction
Excavation
Hydraulic Desilting tunnels
Shihmen Reservoir
1. Amping sluicing tunnel
(Construction is expected to be completed in 2020)
2. Dawanping sluicing tunnel
(In the review, it is expected to be completed in 2029)
Baihe Reservoir sluicing Tunnel
(Construction is expected to be completed in 2019)
Zengwen Reservoir sluicing Tunnel
(in operation)
Nanhua Reservoir sluicing Tunnel
(In construction, it is expected to be completed in 2018)
Hydraulic desilting

## Slide 9
Municipal water
Agricultural water
Industrial water
Annual water consumption in agriculture
Now: 12.6 billion tons
(saving : 6%)
2031: 11.8 billion tons
saving: 800 million tons/yr
3.Water saving- Enhancing conservation for each target
Reduce tap water leakage rate
16% in 2016
10% in 2031
saving: 270 million tons/ yr
In-plant overall recovery rate
Now: 70 %
2031, 80 %
Water recycle use
saving: 50 million tons/yr

## Slide 10
4. Multiple water sources and dispatching backups
Reservoir
Ground
water
Rain water
Desalinated water
River water
Reclaimed water

## Slide 11
Anping Rende Yongkang water recycling centers provide 83,000 tons / day for Southern Science Park Zone in 2025(£ 268,620,000 )
Futian water recycling center provides 130,000 tons / day to Taichung Harbor Industrial Zone in 2025(£ 186,620,000)
Fengshansi reclaimed water plant
In Aug 2018, provides 25,000 tons/ day for Costal Industrial Zone, and estimated 45,000 tons/day in 2019
(£60,120,000 )
Shuinan water recycling center provides 10,000 tons/day for Central Science Park in 2022 (£ 17,580,000)
Fengyuan sewage treatment plant
Planning to provide 20,000 tons / day for water supply to Central Taiwan Science Park (£ 34,300,000 )
Linhai water recycling center provides 33,000 tons / day for Costal Industrial Zone in 2022(£ 91,120,000 )
Taoyuan north district wastewater treatment plant
Planning to provide 40,000 tons / day for Guanyin Industrial Zone in 2025
Wastewater treatment in Hsinchu Industrial Zone
In the BOT outsourcing operation of the Industrial Bureau, the amount of wastewater is 36,000 tons. Plan to provide water to Kinsus.
Kaohsiung
Promote reclaimed water plants all around Taiwan
Prioritize reclaimed water for industrial usage
Reclaimed water-- use each drop twice
Tainan
Hsinchu
Taoyuan
Taichung

## Slide 12
Bills signed on May 29, 2018
River
Rainwater sewerage
Hillside water and soil conservation
Developed land installs runoff distribution facilities.
Land development units set up flood control facilities to absorb increased runoff
detention pond
Urban planning area
Hillside drainage
Local drainage
5. Runoff distribution, outflow regulation

## Slide 13
13
6. Smart water management
Smart Water
Allocation
Smart Security
Facilities
Smart Flood
Prevention
Smart Water
Disclosure
Smart Water
Grid
Smart Irrigation System

## Slide 14
Thank you for listening!
Photoed in Taichung city, Taiwan